## Slide 1
Background & Challenges
2D Vision - Inaccurate estimation of object distance
Non-Linear Dynamics & Leg Control - Translating high-level velocity commands into low-level joint torque
Tightly Coupled Architecture - Vision commands outpace motion control, causing the robot to use stale target data.
Intrinsic Camera Calibration – Accurate calculation of focal length are essential to avoid errors in real-world distance and pose calculations.
BOLT- Behavioral Object Locomotion & Tracking
For Unitree GO2 Robot
Atharva Prabhu, Sahil Sawant (EAS 563 AI Capstone under Prof. David Doermann)
The Problem
Quadruped robots require robust vision-guided navigation to perform autonomous tasks in complex, real-world environments. Unitree Go2, while highly mobile, does not natively provide the autonomous vision-to-motion control required to execute prolonged and responsive behavioral following of dynamic targets.
Our Solution: Implement a real-time autonomous ball-tracking system with sub-50ms latency using decoupled Computer Vision and motion control architecture to perform continuous behavioral following.
Accomplishments
Enabled real time, 3D depth-based object tracking
Closed loop object detection and motion control behavior
Averaging 48ms latency (Worst case 61ms)
Robust and works in multiple environments and lighting.
References: https://github.com/unitreerobotics/unitree_sdk2
Department of Computer Science & Engineering School of Engineering & Applied Sciences
aprabhu5@buffalo.edu | sahilshi@buffalo.edu
Acknowledgments:
A2IL Lab, University at Buffalo | Lab advisors
State-Based Control System
SEARCH: Rotate to find ball (vyaw=0.4)
APPROACH: Fast forward (vx=0.30, d>1.0m)
CREEP: Slow precision (vx=0.15, d<1.0m)
HOLD: Maintain target (vx=0, 0.15m<d<0.5m)
BACKUP: Safety reverse (vx=-0.15, d<0.15m)
Future Applications and Scope
Enhanced multi target tracking
Voice-Guided Tracking & Relocalisation
Challenging Environments
Why it matters:
Search and Rescue operations
Service Robotics
Warehouse Automation
Key Objectives:
Real-time 3D depth-based object tracking
Seamless Computer Vision & Robot Motion
Low latency control loop
Operational Stability
Our Methodology
Camera → Quantized Yolov8n →State Machine → Motion Commands → Robot moves, updating the camera
Limitations
Detection range constraints
Camera Field of View Restrictions
Occlusion
Motion Blur
Learning Outcomes
Facilitating Models on Edge Devices
System Design and Architectures for robots
Hardware Integration
Network Management
End-to-End Deployment
SEARCH
BACKUP
APPROACH/ CREEP